## Slide 1: Four Decades of Automated Image Registration and Segmentation
Koen Van Leemput
April 7, 2022
DSMF symposium - Middelfart

## Slide 2: Automatic segmentation
  Compared to manual delineations:
    Much faster
    More structures
    More repeatable
MRI
segmentation

## Slide 3: Automatic registration
CT
MRI
mosaic
  Local expansion/compression of tissue:
    patient positioning
    bowel/bladder/… filling
    tumor shrinkage
    patient weight loss
    …

## Slide 4: Automatic registration
  Local expansion/compression of tissue:
    patient positioning
    bowel/bladder/… filling
    tumor shrinkage
    patient weight loss
    …
CT
deformed MRI
mosaic
deformation

## Slide 5: Four decades
  1981-2000:
  1996-now: yours truly
    professor at DTU Health Tech
    also affiliated with Massachusetts General Hospital
    highly subjective and biased!

## Slide 6: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 7: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 8: Pre-1980 to 1984
  Analyzing two-dimensional (2D) images
  Low-level image processing:
    “bottom-up” approach
    e.g., region growing, edge detection, …

## Slide 9: 1985-1994: Early days
  3D processing
    Magnetic resonance imaging (MRI)
    Initially 7-10mm slice thickness/spacing…
    Later at higher spatial resolution
    Also 3D PET, SPECT, ultrasound, fast spiral-CT, …

## Slide 10: Registration by aligning corresponding points
  XXXX
    XXX
Match two corresponding point sets defined in two images:
x1
y1
x2
y2
image 1
image 2
rigid: translation + rotation

## Slide 11: Registration by aligning corresponding points
  XXXX
    XXX
Match two corresponding point sets defined in two images:
x1
y1
x2
y2
image 1
image 2
registered image 2

## Slide 12: Multimodal registration-by-segmentation (1989)
  Manually annotate brain surface:
    contours = MRI
    dots = PET
[Pelizarri JCAT 1989]

## Slide 13: Inter-subject registration-by-segmentation (1993)
  Somehow segment brain surface:
    automatically extract “interesting” lines
    try to match lines across brains
[Thirion RR 1993]

## Slide 14: Tissue classification with a neural network (1993)

## Slide 15: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 16: 1995-2014: Model-based methods
  Models:
    “top-down” instead of “bottom-up”
    prior domain knowledge

## Slide 17: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 18: Unimodal deformable registration
subject 1
subject 2

## Slide 19: Unimodal deformable registration: generative model
subject 2
deformed and noisy subject 2
subject 1
≈
random warp and noise
random warp:
- initially fluid mechanics
- later just smoothness

## Slide 20: Unimodal deformable registration
subject 1
subject 2
...
subject N
  Fast filter-based solvers [Thirion MEDIA 1998]

## Slide 21: Unimodal deformable registration
  Fast filter-based solvers [Thirion MEDIA 1998]
subject 1
subject 2
...
subject N

## Slide 22: Unimodal deformable registration
  Fast filter-based solvers [Thirion MEDIA 1998]
subject 2
...
subject N
subject 1

## Slide 23: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 24: Multimodal registration
“good”

## Slide 25: Multimodal registration
“bad”

## Slide 26: Multimodal registration
  With discretized intensities (toy example)
“good”

## Slide 27: Multimodal registration
  With discretized intensities (toy example)
“bad”

## Slide 28: Multimodal registration
  Idea: build a joint histogram
“good”
MRI
CT
CT
MRI

## Slide 29: Multimodal registration
  Idea: build a joint histogram
“bad”
MRI
CT
CT
MRI

## Slide 30: Multimodal registration
  Idea: compute joint entropy
MRI
CT
MRI
CT
lower entropy
higher entropy

## Slide 31: Multimodal registration
MR intensities
CT intensities
“good” = low entropy
[Maes TMI 1997]
[Wells MEDIA 1996]

## Slide 32: Multimodal registration
MR intensities
CT intensities
“bad” = high entropy
[Maes TMI 1997]
[Wells MEDIA 1996]

## Slide 33: Multimodal registration
numerical optimization of entropy

## Slide 34: Multimodal registration
    Modality?
    Scanner?
    Manufacturer?
    Acquisition protocol?
  It doesn’t matter!!

## Slide 35: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 36: Statistical shape models
  Modeling the shape of resistors: 32 corresponding points
“training data”
[Cootes CVIU 1995]

## Slide 37: Statistical shape models
  32*2 = 64-dimensional feature vector
  mean shape
  principal components:
    major modes of variation
    eigenvectors of covariance matrix

## Slide 38: Application in brain segmentation
[Patenaude NeuroImage 2011]

## Slide 39: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 40: Gaussian mixture models
  Voxel-wise segmentation
  Build a cartoon model of the world:
intensity
segmentation label:
- “1” for white matter
- “0” for gray matter

## Slide 41: Gaussian mixture models
  Voxel-wise segmentation
  Build a cartoon model of the world:
intensity
segmentation label:
- “1” for white matter
- “0” for gray matter
model parameters

## Slide 42: Gaussian mixture models

## Slide 43: Gaussian mixture models

## Slide 44: Gaussian mixture models

## Slide 45: Gaussian mixture models

## Slide 46: Gaussian mixture models

## Slide 47: Gaussian mixture models
new subject:
different scanner/protocol

## Slide 48: Gaussian mixture models
new subject:
different scanner/protocol

## Slide 49: Gaussian mixture models
new subject:
different scanner/protocol

## Slide 50: Gaussian mixture models
new subject:
different scanner/protocol
Can adapt to different sequences, scanners, etc

## Slide 51: Gaussian mixture models
  Simple instance of a probabilistic generative model
“anatomical model”
“imaging model”
MRI image
Label image

## Slide 52: Gaussian mixture models
  Simple instance of a probabilistic generative model
“anatomical model”
“imaging model”
MRI image
Label image
model parameters

## Slide 53: Gaussian mixture models
“anatomical model”
“imaging model”
MRI image
Label image
You can’t segment 40+ brain structures with this
Not robust to MR “bias field” artifacts

## Slide 54: Anatomical model
“anatomical model”
“imaging model”
MRI image
Label image
  The parameters control the deformation of “average anatomy”
  Deformation prior
[Ashburner NeuroImage 2005]
[Van Leemput TMI 2009]

## Slide 55: Imaging model
“anatomical model”
“imaging model”
MRI image
Label image
+
Gaussian mixture model
smooth bias field model
[Wells TMI 1996]
[Van Leemput TMI 1999]

## Slide 56: “Inverting” the model
segmentation-by-registration

## Slide 57: “Inverting” the model
segmentation-by-registration

## Slide 58: “Inverting” the model
3T multi-contrast scan
1.5T T1-weighted scans
with manual delineations
(20 subjects)
Training data
[Puonti, NeuroImage 2016]
~5min (CPU)
http://freesurfer.net/

## Slide 59: Adding pathology into the mix…
    Tissue contrast depends on hardware and pulse sequence
    No standard protocol for clinical imaging (multimodal)
    Additional difficulty: Disease-specific lesions!
Lesion

## Slide 60: Idea: alter the generative model
“anatomical model”
“imaging model”
MRI image
Label image
+
Use two anatomical models that are trained on different subjects!

## Slide 61
[Agn MEDIA 2019]
Radiation therapy planning

## Slide 62
Radiation therapy planning
[Agn MEDIA 2019]

## Slide 63
Radiation therapy planning
[Agn MEDIA 2019]

## Slide 64: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 65: Level sets (late 1990s – early 2000s)
  Implicit surface representations
    E.g., embed a 2D curve as an iso-level in a 3D surface
[Zeng MICCAI 1998]

## Slide 66: Diffeomorphic registration (mid-late 2000s)
  Deformation fields should be smooth and invertible
    Integration over artificial time
[Beg IJCV 2005]
[Ashburner NeuroImage 2007]
[Avants MEDIA 2008]
[Vercauteren NeuroImage 2009]

## Slide 67: Diffeomorphic registration (mid-late 2000s)
  Deformation fields should be smooth and invertible
    Integration over artificial time
deformation field
[Beg IJCV 2005]
[Ashburner NeuroImage 2007]
[Avants MEDIA 2008]
[Vercauteren NeuroImage 2009]

## Slide 68: Multi-atlas label fusion (2005-2014)
  Pure segmentation-by-registration
image to be segmented
scan 1
segmentation 1
[Heckemann NeuroImage 2006]

## Slide 69: Multi-atlas label fusion (2005-2014)
  Pure segmentation-by-registration
image to be segmented
scan 1
segmentation 1
Compute the deformation between the image and scan 1
[Heckemann NeuroImage 2006]

## Slide 70: Multi-atlas label fusion (2005-2014)
  Pure segmentation-by-registration
Apply the deformation to segmentation 1
image to be segmented
warped scan 1
warped segmentation 1
[Heckemann NeuroImage 2006]

## Slide 71: Multi-atlas label fusion (2005-2014)
Repeat for all N training subjects
...
...
image to be segmented
warped scan 1
warped segmentation 1
warped scan N
warped segmentation N
  Pure segmentation-by-registration
[Heckemann NeuroImage 2006]

## Slide 72: Multi-atlas label fusion (2005-2014)
...
...
image to be segmented
warped scan 1
warped segmentation 1
warped scan N
warped segmentation N
Combine the results somehow
  Pure segmentation-by-registration
[Heckemann NeuroImage 2006]

## Slide 73: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 74: Segmenting a brain scan with “machine learning”
  voxel-wise segmentation:
Training data
intensity
segmentation label:
- “1” for white matter
- “0” for gray matter

## Slide 75: Segmenting a brain scan with “machine learning”
  voxel-wise segmentation:
Training data
intensity
segmentation label:
- “1” for white matter
- “0” for gray matter

## Slide 76: Segmenting a brain scan with “machine learning”

## Slide 77: Segmenting a brain scan with “machine learning”
tunable “weights”
“squash” function

## Slide 78: Segmenting a brain scan with “machine learning”

## Slide 79: Segmenting a brain scan with “machine learning”

## Slide 80: Segmenting a brain scan with “machine learning”

## Slide 81: Segmenting a brain scan with “machine learning”
new subject:
same scanner/protocol

## Slide 82: Segmenting a brain scan with “machine learning”
new subject:
same scanner/protocol

## Slide 83: Segmenting a brain scan with “machine learning”
new subject:
same scanner/protocol

## Slide 84: Segmenting a brain scan with “machine learning”
new subject:
same scanner/protocol
- No models needed
- Simply learn from training examples

## Slide 85: Segmenting a brain scan with “machine learning”
new subject:
different scanner/protocol

## Slide 86: Segmenting a brain scan with “machine learning”
new subject:
different scanner/protocol

## Slide 87: Segmenting a brain scan with “machine learning”
new subject:
different scanner/protocol
Need matching training examples

## Slide 88: Deep learning
  Looks at entire images or image patches (instead of one voxel at a time)
  Basis functions are estimated from training data as well
[Ronneberger MICCAI 2015]

## Slide 89: Deep learning
- No domain-specific expertise required
- Easy (PyTorch/TensorFlow/…)
- Fast!! (GPU)
[Isensee Nature Comm. 2021]

## Slide 90: Deep learning
- No domain-specific expertise required
- Easy (PyTorch/TensorFlow/…)
- Fast!! (GPU)
[Isensee Nature Comm. 2021]
Siemens Vision 1.5T MPRAGE
GE Signa 1.5T SPGR
Siemens Tim Trio 3T MPRAGE

## Slide 91: Synthetic training data
  Run old-style generative models only in the forward direction
    training time 1 week (GPU)
    contrast-invariance
    only 1mm isotropic voxels
  But combinatorics?
    image resolution?
    multi-contrast?
    pathology?
[Billot 2021]

## Slide 92: Overview
Pre-1980 to 1994: humble beginnings
1995-2014: model-based techniques:
  Unimodal deformable registration
  Multimodal registration
  Statistical shape models
  Segmentation using generative models
  Hyped-up topics
2015-now: learning from examples
Future outlook

## Slide 93: The past…
...
volunteer 1
volunteer 2
volunteer 1
volunteer 3
volunteer 300
  Past few decades: scientific group studies
- Research focus (healthy-looking, high quality and standardized scans)
- Software is available
- Much faster but also more errors than human experts

## Slide 94: … vs. the future
  New frontier: clinical practice
patient John Doe
Best treatment for John?

## Slide 95
Poor image quality?
Imaging not standardized?
Pathology?
- Errors still OK?
- Uncertainty?