## Slide 1: Intermediate Deformable Image Registration via Windowed Cross-Correlation
Iman Aganj and Bruce Fischl
Athinoula A. Martinos Center for Biomedical Imaging
Massachusetts General Hospital
Harvard Medical School

## Slide 2
Initialization of Deformable Registration
Problem:
  Deformable registration may miss the global optimum.
A solution:
  Initialize with the results of affine (linear) registration.
Drawback:
  Affine is too simple and does not account for anatomical variation.
Proposed solution:
  Initialize with Intermediate Deformable Image Registration (IDIR).
Notes: In a common approach to achieve symmetry, both images are deformed and compared in a mid-space, which makes the registration invariant with respect to the ordering of the images. Such methods essentially minimize their cost functions with respect to two transformations 𝑇_1 and 𝑇_2 that take the two input images to the mid-space. Without additional constraints, however, this increases the degrees of freedom of the problem twofold, since the end result of pairwise registration is really one transformation, 𝑇=𝑇_2∘𝑇_1^(−1), that takes the second input image to the first. In addition, the mid-space can drift arbitrarily far away from the native spaces of the images, for example due to large changes in 𝑇_1 and 𝑇_2, which decreases the mid-space cost function without changing the final transformation 𝑇. To alleviate these issues, some additional anti-drift constraints are used to keep the mid-space “in between” the native spaces of the two images. For example, they may restrict 𝑇_1 and 𝑇_2 to have opposite displacement fields, or to be the inverse of each other. The choice of the anti-drift constraints may bias the registration algorithm towards favoring a particular set of transformations, and therefore affect the results.

## Slide 3
Cross-Correlation of Phase Images
Cross-correlation of the images
Cross-correlation of the phase images
(Kuglin and Hines, ICCS’75; Pearson et al, ATS’77)
: | Number of pixels
 | Number of pixels
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 4
Moving Window Function
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 5
Windowed Cross-Correlation
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 6
Computational Complexity
: | Number of pixels
 | Number of pixels
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 7
Computational Complexity Reduction
: | Images
 | Images
: | Window function
 | Window function
: | Center of the window
 | Center of the window
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 8
Computational Complexity Reduction
: | Images
 | Images
: | Window function
 | Window function
: | Center of the window
 | Center of the window
: | Displacement field
 | Displacement field
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 9
Approximating
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 10
: | Number of pixels
: | Image dimension
 | Number of pixels
 | Image dimension
Computational Complexity Reduction
: | Center of the window
 | Center of the window
: | Displacement field
 | Displacement field
Notes: A change of variables and further calculation reveal that the data term is, remarkably, only a function of 𝑇, the transformation that takes one image to the other. So, we can minimize this data term directly with respect to 𝑇, as opposed to the previous methods that optimize their cost functions with respect to both 𝑇_1 and 𝑇_2, conditioned to constraints that prevent the mid-space drift. With this data term being independent of 𝑇_1 and 𝑇_2, the mid-space disappears, also eliminating the problem of the mid-space drift. We don’t need to enforce any anti-drift constraints anymore, and we won’t bias the space of possible transformations by the particular choice of such constraints. This is all while keeping the degrees of freedom of the optimization half of that of the unconstrained problem of solving for both 𝑇_1 and 𝑇_2. In addition, one can verify the symmetry of this data term, which, however, holds only in the continuous domain. In the discrete case, where one image is resampled and the other is not, discretization artifacts may produce a bias.

## Slide 11
Results of IDIR
2D X-Ray Registration
Original | Iteration 1 | Iteration 2 | Iteration 20
Data source: https://lytornado.pixnet.net/blog/post/266239880-%40地包天%28戽斗%29牙齒矯正注意事項
Before/After Surgery
Notes: In a common approach to achieve symmetry, both images are deformed and compared in a mid-space, which makes the registration invariant with respect to the ordering of the images. Such methods essentially minimize their cost functions with respect to two transformations 𝑇_1 and 𝑇_2 that take the two input images to the mid-space. Without additional constraints, however, this increases the degrees of freedom of the problem twofold, since the end result of pairwise registration is really one transformation, 𝑇=𝑇_2∘𝑇_1^(−1), that takes the second input image to the first. In addition, the mid-space can drift arbitrarily far away from the native spaces of the images, for example due to large changes in 𝑇_1 and 𝑇_2, which decreases the mid-space cost function without changing the final transformation 𝑇. To alleviate these issues, some additional anti-drift constraints are used to keep the mid-space “in between” the native spaces of the two images. For example, they may restrict 𝑇_1 and 𝑇_2 to have opposite displacement fields, or to be the inverse of each other. The choice of the anti-drift constraints may bias the registration algorithm towards favoring a particular set of transformations, and therefore affect the results.

## Slide 12
Results of IDIR
2D X-Ray Registration
Original | Iteration 1 | Iteration 2 | Iteration 20
Data source: https://www.chelwest.nhs.uk/your-visit/patient-leaflets/surgery-services/midfoot-problems
Before/After Surgery
Notes: In a common approach to achieve symmetry, both images are deformed and compared in a mid-space, which makes the registration invariant with respect to the ordering of the images. Such methods essentially minimize their cost functions with respect to two transformations 𝑇_1 and 𝑇_2 that take the two input images to the mid-space. Without additional constraints, however, this increases the degrees of freedom of the problem twofold, since the end result of pairwise registration is really one transformation, 𝑇, that takes the second input image to the first. In addition, the mid-space can drift arbitrarily far away from the native spaces of the images. To alleviate these issues, some additional anti-drift constraints are used to keep the mid-space “in between” the native spaces of the two images. For example, they may restrict 𝑇_1 and 𝑇_2 to have opposite displacement fields, or to be the inverse of each other. The choice of the anti-drift constraints may bias the registration algorithm towards favoring a particular set of transformations, and therefore affect the results.

## Slide 13
Results of IDIR
3D Fetal MRI Registration
Original | Iteration 1 | Iteration 2 | Iteration 3 | Iteration 50
Data source: Gholipour et al, “A normative spatiotemporal MRI atlas of the fetal brain for automatic segmentation and analysis of early brain growth,” Scientific Reports, 2017.
Week 21
Week 38
Notes: In a common approach to achieve symmetry, both images are deformed and compared in a mid-space, which makes the registration invariant with respect to the ordering of the images. Such methods essentially minimize their cost functions with respect to two transformations 𝑇_1 and 𝑇_2 that take the two input images to the mid-space. Without additional constraints, however, this increases the degrees of freedom of the problem twofold, since the end result of pairwise registration is really one transformation, 𝑇, that takes the second input image to the first. In addition, the mid-space can drift arbitrarily far away from the native spaces of the images. To alleviate these issues, some additional anti-drift constraints are used to keep the mid-space “in between” the native spaces of the two images. For example, they may restrict 𝑇_1 and 𝑇_2 to have opposite displacement fields, or to be the inverse of each other. The choice of the anti-drift constraints may bias the registration algorithm towards favoring a particular set of transformations, and therefore affect the results.

## Slide 14
Results of IDIR
3D Fetal MRI Registration
Data source: Gholipour et al, “A normative spatiotemporal MRI atlas of the fetal brain for automatic segmentation and analysis of early brain growth,” Scientific Reports, 2017.
Overlap of 116 labels
Diffeomorphic demons with three resolution levels:
0.76
After initialization with IDIR:
0.80
Notes: In a common approach to achieve symmetry, both images are deformed and compared in a mid-space, which makes the registration invariant with respect to the ordering of the images. Such methods essentially minimize their cost functions with respect to two transformations 𝑇_1 and 𝑇_2 that take the two input images to the mid-space. Without additional constraints, however, this increases the degrees of freedom of the problem twofold, since the end result of pairwise registration is really one transformation, 𝑇, that takes the second input image to the first. In addition, the mid-space can drift arbitrarily far away from the native spaces of the images. To alleviate these issues, some additional anti-drift constraints are used to keep the mid-space “in between” the native spaces of the two images. For example, they may restrict 𝑇_1 and 𝑇_2 to have opposite displacement fields, or to be the inverse of each other. The choice of the anti-drift constraints may bias the registration algorithm towards favoring a particular set of transformations, and therefore affect the results.

## Slide 15
Intermediate Deformable Image Registration (IDIR)
  Suitable for initializing deformable registration:
    More flexible than affine registration
    Less flexible than standard deformable registration
  Computationally efficient:
    Moderately low computational complexity
    Alignment of the bulk of deformation within a few iterations
Notes: In a common approach to achieve symmetry, both images are deformed and compared in a mid-space, which makes the registration invariant with respect to the ordering of the images. Such methods essentially minimize their cost functions with respect to two transformations 𝑇_1 and 𝑇_2 that take the two input images to the mid-space. Without additional constraints, however, this increases the degrees of freedom of the problem twofold, since the end result of pairwise registration is really one transformation, 𝑇=𝑇_2∘𝑇_1^(−1), that takes the second input image to the first. In addition, the mid-space can drift arbitrarily far away from the native spaces of the images, for example due to large changes in 𝑇_1 and 𝑇_2, which decreases the mid-space cost function without changing the final transformation 𝑇. To alleviate these issues, some additional anti-drift constraints are used to keep the mid-space “in between” the native spaces of the two images. For example, they may restrict 𝑇_1 and 𝑇_2 to have opposite displacement fields, or to be the inverse of each other. The choice of the anti-drift constraints may bias the registration algorithm towards favoring a particular set of transformations, and therefore affect the results.

## Slide 16
Thank You!
http://iman.mgh.harvard.edu
Code: www.nitrc.org/projects/msi-register